## Slide 1: Dealing with different/ uneven sampling rates
BEP029
TC 8th October, 2020
Sein Jeung, Julius Welzel, Robert Oostenveld

## Slide 2: Survey results

## Slide 3: Current status
“[… Recordings with different sampling frequencies and/or starting times should be stored in separate files. …] “ (BIDS 1.4.1 - Physiological and other continuous recordings)
Eye Tracking , different sampling rates for each eye (BEP020)
 Use events for clarification (Helenas approach)

## Slide 4: Example
time
‚start_imu_1‘
‚start_imu_2‘
‚stop_imu_1‘
‚stop_imu_2‘
Events 100 Hz
Camera 1 (Optical) 300 Hz
IMU 1 Acc 222 Hz
IMU 1 Gyro 100 Hz
IMU 2 Gyro 100 Hz
IMU 2 Acc 100 Hz
‚start_camera_1‘
‚stop_camera_1‘
IMU 2 Mag 100 Hz

## Slide 5: BIDS directory structure (_channels.tsv)
IMU 1
  Acc
    X
    Y
    Z
  Gyro
    X
    Y
    Z
IMU 2
  Acc
    X
    Y
    Z
  Gyro
    X
    Y
    Z
Optical
  Pos
    X
    Y
    Z
name | source | type | component | unit | location | Sampling frequency
Imu_1_acc_x | Imu 1 | acceleration | x | m/s² | 5.3-432 | 222 Hz
Imu_2_acc_y | Imu 2 | acceleration | y | m/s² | 6.3-432 | 120 Hz
Imu_2_gyro_x | Imu 2 | angluar velocity | x | °/s | 6.3-432 | 100 Hz
Optical_1_pos_z | Tracker 1 | position | z | m | 6.3-432 | 300 Hz

## Slide 6: Open questions?
Resample to highest sampling rate within entity (acceleration)
Location for optical and other systems
Organization of “electrode” description
Location description (“electrodes”) can be used in for defining events
…

## Slide 7
IMU 1
  Acc (200 Hz)
    X
    Y
    Z
  Gyro (100 Hz)
    X
    Y
    Z
  Magn (200 Hz)
    X
    Y
    Z
IMU 2
  Acc (100 Hz)
    X
    Y
    Z
  Gyro (100 Hz)
    X
    Y
    Z